## Slide 1
Hands-On With Monte Carlo Simulations
Mohammad Soroush Barhaghi†, Younes Nejahi‡, Loren Schwiebert‡, and Jeffrey Potoff†
† Department of Chemical Engineering & Materials Science, College of Engineering,
‡ Department of Computer Science, College of Engineering, Wayne State University, Detroit, MI,
USA 48202
Notes: 1- MC simulation engine
2- Developed by potoff group & schwibert
3- Developed for running on CPU and GPU
4- CPU system size < 10,000
5- GPU system size > 10,000

## Slide 2: Tutorial files
On GitHub
Git clone https://github.com/ GOMC-WSU /Workshop.git
Website https://github.com/GOMC-WSU/Workshop/tree/AIChE2019
To run example: change the directory to ~/GOMC-Workshop/

## Slide 3: Overview
Grand canonical Monte Carlo simulation
  Adsorption of Ar and CO2 in IRMOF-1
    System setup for adsorption in porous materials, using automated HTS tools
    Modify the XML input file to HTS tools
    Add new adsorbate molecule
    Extract the simulation results
Canonical Monte Carlo simulation.
  Solvation free energy of Ne, Ar, and Kr in cyclohexane
    System setup for free energy calculation
    Define the lambda states and soft-core parameters
    Calculate the solvation free energy with TI and FEP estimators

## Slide 4: Acknowledgements
Jason Mick, Younes Nejahi, Kamel Rushaidat, Niloofar Torabi, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, OAC-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU

## Slide 5: Introduction to GOMC

## Slide 6
NVT, NPT, GCMC,
and GEMC
Linear, Branched, cyclic, and Polar molecules
Martini
Charmm
OPLS
Mie
Exp-6
CPU
OpenMP
GPU
OpenMP + GPU
Parallelization
Moves Supported:
Displacement
Rotation
Swap; Intra-swap (CD-CBMC)
Regrowth (CD-CBMC)
MEMC (inter/intra)
Multi-particle move
Free energy calculations
Volume (isotropic, anisotropic)

## Slide 7: GOMC I/O
PDB
PSF
Parameter
Control
Log
PDB
PSF
Block Averages
GCMC: Histogram

## Slide 8: GOMC I/O: Input
PDB
PSF
Parameter
Control
Coordinates of all atoms
Connectivity between atoms and partial charges.
Maps atom names to atom types
Bonded and non-bonded parameters for all atoms,
bonds, angles and dihedrals
Simulation run conditions: box size, temperature
Move ratios, parameter files, etc.

## Slide 9: Generating PDB file
PACKMOL
Single molecule
PDB file
Packed molecule
PDB file
Packing information:
Num. molecule
Box size

## Slide 10: Generating PSF file
VMD
Packed molecule
PDB file
PDB and PSF file
Topology file :
Atom type, charge
bonds

## Slide 11: Grand Canonical Monte Carlo Example

## Slide 12: Grand Canonical Monte Carlo
Acceptance criteria for molecule swap in Grand Canonical ensemble Monte Carlo (GCMC).
Chemical Potential (K)
Fugacity (bar)

## Slide 13: Creating PDB/PSF for adsorbent, manually:
Beta Value
  Beta = 0: Displace, Rotate, Intra-swap, Swap, regrowth
  Beta = 1: Fix position
  Beta = 2: Displace, Rotate, Intra-swap, regrowth
Tcl script in VMD
AIChE 2018 workshop: https://github.com/GOMC-WSU/Workshop
Notes: Tell them how hard it is to setup the simulation for adsorption manually.

## Slide 14: Creating adsorption simulation file, automatically:
Computation-Ready, Experimental Metal–Organic Frameworks: A Tool To Enable High-Throughput Screening of Nanoporous Crystals, Chem. Mater. 2014, 26, 21, 6185-6192
HTS
XML input file
Notes: More than 5000 MOFs

## Slide 15
HTS
Read CIF file and generate PDB, PSF for MOFs:
_cell_length_a 18.26599998
_cell_length_b 18.26600037
_cell_length_c 18.26600000
_cell_angle_alpha 60.00000067
_cell_angle_beta 59.99999996
_cell_angle_gamma 60.00000068
Zn 0.29338 0.29338 0.29338 1.103633
Zn 0.29338 0.29338 0.11986 1.103633
H 0.1546 0.4552 0.4552 0.115883
H 0.4552 0.1546 0.935 0.115883
C 0.0927 0.4731 0.4731 -0.055959
C 0.4731 0.0927 0.9611 -0.055959
Reading the cell dimension
Calculate the cell basis vectors
Calculate the min. cell extension using the cutoff value
Extend the unit cell
Create the PDB file for MOFs
Detect the unique atom charges
Create the topology for MOFs
Create the PSB file for MOFs
Notes: Charge are DFT-optimized in ddec

## Slide 16: HTS XML input file
XML input file
System: General information of the system
  Model name
  Adsorbent information (HTS or single adsorption)
  Adsorbate information (Reservoir information)
Simulation: Simulation parameters that are fixed for all runs
  MC steps
  LJ and coulomb cutoff
  Electrostatic calculation parameters
  GOMC outputs frequency
Run simulation: Simulation parameters that are flexible for each runs
  Temperature
  Fugacity

## Slide 17: HTS XML input file
System
Simulation
Run simulation
Notes: By now they should understand the fields in xml file

## Slide 18: Grand Canonical Monte Carlo Example
Setup simulation files for Ar adsorption in IRMOF-1 (EDUSIF)
  Modify the HTS XML file to define our simulation parameters.
  Simulation of Ar adsorption in IRMOF-1 at 298 K , 1.0, and 10.0 bar.
  Calculate the number of Ar adsorbed.
Setup simulation files for CO2 adsorption in IRMOF-1 (EDUSIF)
  Add topology and force field parameters for CO2 to HTS tool.
  Simulation of CO2 adsorption in IRMOF-1 at 298 K, 1.0, and 10.0 bar.
  Calculate the number of CO2 adsorbed.

## Slide 19: Task 1: Modifying the ConfigSetup.xml
Go to adsorption/AR_IRMOF1/.
Open the ConfigSetup.xml with a text editor
Replace the “Fill-by-user” with correct string or value
Our goal is to
Simulate argon adsorption in IRMOF at 298 K and two different pressures
Argon pdb name is “argon.pdb”
Argon resname is “AR”
We want to pack 1000 argon in 60 A box
Pressure 1.0 bar and 10.0 bar

## Slide 20: Task 1: Modifying the ConfigSetup.xml
Here are the fields that need to be changed in the XML files:
Notes: Show them where they need to modify

## Slide 21: Task 1: Modifying the ConfigSetup.xml
Here is the correct changes to the XML files:
Now run the simulation_setup.py to generate the simulation files.
Follow the README.txt
Notes: Make sure everyone have modified the xml file correctly

## Slide 22: HTS directory setup
run_files
EDUSIF
common
RUN1
RUN2
MOF_base
reservoir_base
...
...
Notes: Show them how HTS will setup the directory for them

## Slide 23: Control file: GCMC
# INPUT PDB, PSF FILES
Coordinates 0 ../common/MOF_base/EDUSIF_BOX_0.pdb
Coordinates 1 ../common/reservoir_base/START_BOX_1.pdb Structure 0 ../common/MOF_base/EDUSIF_BOX_0.psf
Structure 1 ../common/reservoir_base/START_BOX_1.psf
# MOVE FREQUENCY
DisFreq 0.30
RotFreq 0.20
SwapFreq 0.50
# Chemical Potential/Fugacity
Fugacity AR 1.0
Fugacity EDUS 0.0
Vector1
Vector2
Vector3
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 36.5320 0.0000 0.0000
CellBasisVector2 0 18.2660 31.6376 0.0000
CellBasisVector3 0 18.2660 10.5459 29.8283
CellBasisVector1 1 60 0.00 0.00
CellBasisVector2 1 0.00 60 0.00
CellBasisVector3 1 0.00 0.00 60
# OutHistSettings
DistName dis
HistName his
RunNumber 1
RunLetter a
SampleFreq 200
Notes: Ask them to take a look a the config file for run_files/EDUSIF/RUN1-FUGACITY-1.0-TEMPERATURE-298/in.conf

## Slide 24: GOMC I/O: LOG Output
80
Notes: Before extracting the data, show tell them about console output

## Slide 25: GOMC I/O: BLOCK Output
Notes: Before extracting the data, show tell them about Block output

## Slide 26: GOMC I/O: LOG Output
MOVE_<box number>: move statistics
ENER_<box number>: energies
STAT_<box number>: density
Data are stored in columns, making them straightforward to extract with awk.
Quantities are instantaneous values, and are defined with MTITLE, ETITLE and STITLE headers near the beginning of the log file.
Notes: Talk about output file when Production is running!

## Slide 27: GOMC I/O: GCMC
Extract data using awk
  cat output_AR.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_AR_fluct.dat

## Slide 28: GOMC I/O: GCMC
Extract data using awk
  cat output_AR.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_AR_fluct.dat

## Slide 29
HTS
Generate PDB, PSF file for reservoir:
Pack the adsorbate molecules
Create PDB for reservoir
Create PSF for reservoir
Single molecule
PDB file
Topology file
PACKMOL
VMD
Notes: HTS need the single molecule PDB and topology file for adsorbate, to generate the PDB and PSF file.

## Slide 30
BUILD/
Add New Adsorbate to HTS:
model/
pdb/
Top_adsorbate.inp
Parameters_Universal.par
. . .
Add adsorbate topology to this file.
Add force field parameter this file.
Add a single adsorbate PDB file to this directory.
Notes: There are more directories in the BUILD, but to add a new adsorbate, we just need to:
1- Add single pdb file to “pdb” directory
2- Add the adsorbate topology and parameter file

## Slide 31: Task 2: Add CO2 adsorbate to HTS
Go to adsorption/CO2_IRMOF1/.
We already added the single CO2 pdb file (carbondioxide.pdb) to “BUILD/” directory
You need to add the CO2 topology to “BUILD/molel/Top_adsorbate.inp”
You need to add the CO2 force field parameters to “BUILD/molel/Parameters_Universal.par”
REMARK Single pdb file for carbon dioxide
ATOM 1 O1 CO2 A 1 00.000 00.000 00.000 1.00 0.00 CO2 O
ATOM 2 C1 CO2 A 1 01.160 00.000 00.000 1.00 0.00 CO2 C
ATOM 3 O2 CO2 A 1 02.320 00.000 00.000 1.00 0.00 CO2 O

## Slide 32: Topology file
RESI SPCE 0.00
GROUP
ATOM O1 OT -0.847600 ! O1
ATOM H1 HT 0.423800 ! / \
ATOM H2 HT 0.423800 ! H1 H2
BOND O1 H1 O1 H2
PATCHING FIRS NONE LAST NONE
Defines residue name
Maps atom name to atom type
Column 3 is the partial charge
Defines bonds between pairs of atoms.
Atom type
Atom name
Partial charges
Notes: Teach them about topology file

## Slide 33: Task 2.1: Add CO2 topology to Top_adsorbate.inp
Open to “BUILD/molel/Top_adsorbate.inp” with a text editor.
Replace “Fill-by-user” with the correct structural information.
name: O1
type: O2C
Charge: -0.35
name: O2
type: O2C
Charge: -0.35
name: C1
type: CO2
Charge: +0.70
RESI CO2 0.00 !
GROUP
Fill-by-user
PATCHING FIRS NONE LAST NONE
Resname CO2

## Slide 34: Task 2.1: Add CO2 topology to Top_adsorbate.inp
Here is the correct changes to the Top_adsorbate.inp file:
RESI CO2 0.00 ! GROUP
ATOM O1 O2C -0.35
ATOM C1 CO2 0.70
ATOM O2 O2C -0.35
BOND O1 C1 C1 O2
PATCHING FIRS NONE LAST NONE
name: O1
type: O2C
Charge: -0.35
name: O2
type: O2C
Charge: -0.35
name: C1
type: CO2
Charge: +0.70

## Slide 35: Task 2: Add CO2 adsorbate to HTS
Go to adsorption/CO2_IRMOF1/.
We already added the single CO2 pdb file (carbondioxide.pdb) to “BUILD/” directory
We added the CO2 topology to “BUILD/molel/Top_adsorbate.inp”
You need to add the CO2 force field parameters to “BUILD/molel/Parameters_Universal.par”
Notes: Transition to what to do next, setting up the parameter file

## Slide 36: Parameter file: Bonds and Angles
BONDS
!
!V(bond) = Kb(b - b0)**2
!
!atom type Kb(K/mole/A**2) b0 (A) description
OT HT 9999999999 1.000 ! Fixed.
ANGLES
!
!V(angle) = Ktheta(Theta - Theta0)**2!
!
!atom types Ktheta(K/mole/rad**2) Theta0(degree)
HT OT HT 9999999999 109.50 ! fixed
Notes: Teach them how to set the bonds and angle parameter, specially how to fix the bond and angle.

## Slide 37: Parameter file: Nonbonded
EXOTIC
NONBONDED_MIE
!
! V(mie) = 4*eps*((sig_ij/r_ij)**n-(sig_ij/r_ij)**6)
!
!atom type eps(K) sigma(A) n eps,1-4(K) sigma,1-4(A) n,1-4 !description
OT 78.2054 3.167 12 0.00 0.000 0 ! SPCE
HT 0.0000 0.000 12 0.00 0.000 0 ! SPCE
Notes: Teach them how to set the nonbonded parameters

## Slide 38: Task 2.2: Add CO2 force field parameter to Parameters_Universal.par
Open to “BUILD/molel/Parameters_Universal.par” with a text editor.
Replace “Fill-by-user” with the correct bonded and non-bonded parameters.
type: O2C
type: O2C
type: CO2
BONDS
!atom type Kb b0
Fill-by-user
ANGLES
!atom types Ktheta Theta0
Fill-by-user
NONBONDED_MIE
! Atom type eps sig n eps1-4 sig1-4 n1-4
Fill-by-user
O-C bond: 1.16 A, fix
O-C-O angle: 180, fix

## Slide 39: Task 2.2: Add CO2 force field parameter to Parameters_Universal.par
BONDS
!atom type Kb b0
CO2 O2C 9999999999999 1.16
ANGLES
!atom types Ktheta Theta0
O2C CO2 O2C 9999999999999 180.00
NONBONDED_MIE
! Atom type eps sig n eps1-4 sig1-4 n1-4
O2C 79.00 3.050 12 0.0 0.0 0.0
CO2 27.00 2.800 12 0.0 0.0 0.0
Here is the correct changes to the Top_adsorbate.inp file:
type: O2C
type: O2C
type: CO2
O-C bond: 1.16 A, fix
O-C-O angle: 180, fix

## Slide 40: Task 2: Add CO2 adsorbate to HTS
Go to adsorption/CO2_IRMOF1/.
We already added the single CO2 pdb file (carbondioxide.pdb) to “BUILD/” directory
We added the CO2 topology to “BUILD/molel/Top_adsorbate.inp”
We added the CO2 force field parameters to “BUILD/molel/Parameters_Universal.par”
Now run the simulation_setup.py to generate the simulation files.
Follow the README.txt
Notes: Transition to what to do next, setting up the simulation files

## Slide 41: GOMC I/O: GCMC
Extract data using awk
  cat output_CO2.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_CO2_fluct.dat

## Slide 42: GOMC I/O: GCMC
Extract data using awk
  cat output_CO2.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_CO2_fluct.dat

## Slide 43
Free Energy Calculation

## Slide 44
= Full interaction
= No interaction
Free energy calculation: FEP

## Slide 45
Free energy calculation: FEP/TI

## Slide 46
Figure: T. Steinbrecher, I. Joung, and D. A. Case, J. Comput. Chem. 32 (15), 3253 (2011).
Free energy calculation: Scale nonbonded Interaction

## Slide 47
Free energy calculation: FEP/TI

## Slide 48: Free energy calculation: FEP/TI
Solvation free energy of Ne in cyclohexane at 298 K and 1.0 bar
  NVT simulation in 4 intermediate states
  Calculate Ne solvation free energy in cyclohexane with alchemlyb
  Calculate Ne solvation free energy in cyclohexane with alchemical-analysis
Solvation free energy of Ar in cyclohexane at 298 K and 1.0 bar
  Setup GOMC config file and run NVT simulation in 4 intermediate states
  Calculate Ar solvation free energy in cyclohexane with alchemlyb
  Calculate Ar solvation free energy in cyclohexane with alchemical-analysis
https://github.com/alchemistry/alchemlyb
https://github.com/msoroush/alchemical-analysis

## Slide 49: Free energy calculation: Simulation Process
NVT at 298 K
NPT at 298 K,
1.0 bar
NVT at 298 K,
NPT at 298 K,
1.0 bar,
Pack solvent + 1 solute
alchemlyb,
alchemical-analysis
https://github.com/msoroush/alchemical-analysis
https://github.com/alchemistry/alchemlyb
Notes: Green box means, we already performed the simulation
Red box means, they should do it in the workshop

## Slide 50: Control file: Free Energy calculation
Restart true
Coordinates 0 ./EQ_BOX_0_restart.pdb
Structure 0 ./EQ_merged.psf
# FREE ENERGY PARAMETER
FreeEnergyCalc true 1000
MoleculeType NE 1
InitialState 1
ScalePower 2
ScaleAlpha 0.5
MinSigma 3.0
ScaleCoulomb false
LambdaVDW 0.00 0.20 0.40 0.60 0.8 1.00 1.00 1.00 1.00 1.00 1.00
LambdaCoulomb 0.00 0.00 0.00 0.00 0.00 0.00 0.20 0.40 0.60 0.80 1.00
Notes: You need to explain them which keyword means what. Most importantly, the initialState and LmabdaVDW keyword.

## Slide 51: Task 1: Running free energy calculation simulation.
Go to freeEnergy/NE/.
Run the NVT simulation at 4 intermediate states. (Follow the README.txt)
  states/state_0
  states/state_1
  states/state_2
  states/state_3
Take a look at prod.conf file in each state to learn about free energy parameters.
FreeEnergyCalc true 1000
MoleculeType NE 1
ScalePower 2
ScaleAlpha 0.5
MinSigma 3.0
InitialState 0
LambdaVDW 0.00 0.22 0.70 1.00
FreeEnergyCalc true 1000
MoleculeType NE 1
ScalePower 2
ScaleAlpha 0.5
MinSigma 3.0
InitialState 3
LambdaVDW 0.00 0.22 0.70 1.00
. . .
Notes: Teach them how in GOMC they can specify which intermediate states runs the NVT ( by setting InitialState 0, 1, … 3)

## Slide 52
(K) |  |  |  |  |  |  |  |  | 
Steps |  |  |  |  |  |  | … |  | 
1000 | -8877.456 | -3.231 | 8.077 | 10.004 | 2.624 | 0.000 | … | 2266.677 | 3.181
2000 | -8835.898 | 2.683 | 110.732 | -0.256 | -4.425 | 0.000 | … | 47079.538 | 3.164
3000 | -8827.969 | 1.666 | 245.945 | -14.514 | -14.142 | 0.000 | … | 19780.139 | 3.188
… | … | … | … | … | … | … | … | … | …
10000 | -8819.957 | -11.471 | 37.901 | 6.680 | 0.422 | 0.000 | … | 1383.572 | 3.171
Steps |  |  |  |  |  |  | … |  | 
1000 | -8877.456 | -3.231 | 8.077 | 10.004 | 2.624 | 0.000 | … | 2266.677 | 3.181
2000 | -8835.898 | 2.683 | 110.732 | -0.256 | -4.425 | 0.000 | … | 47079.538 | 3.164
3000 | -8827.969 | 1.666 | 245.945 | -14.514 | -14.142 | 0.000 | … | 19780.139 | 3.188
… | … | … | … | … | … | … | … | … | …
10000 | -8819.957 | -11.471 | 37.901 | 6.680 | 0.422 | 0.000 | … | 1383.572 | 3.171
Table: Sample of GOMC free energy data
GOMC Free Energy Output
Notes: Teach them how GOMC will calculate the du/dlambda and change in energy between current states and all other states.
Tell them BAR estimator needs only change in energy between neighboring states, but MBAR needs between all other states

## Slide 53: Task 2: Analysis the GOMC free energy outputs.
Go to freeEnergy/NE/result/.
Copy the free energy files into "data" directory
  “cp ../states/state*/Free_Energy_BOX_0_PRODUCTION_*.dat ./data/.”
Calculate the solvation free energy with alchemlyb library
  “python ./free_energy_calc.py”
Plot the solvation free energy with alchemical_analysis tool
  “alchemical_analysis -a gomc -d data -p Free_Energy_BOX_0_PRODUCTION_ -q dat -g True -w True -f 10 -u 'kcal' -o plots -m '-DEXP-IEXP’ ”
Notes: Tell them that they can copy and paste the command from README.txt file

## Slide 54
Ne Solvation Free Energy: 4 States
Notes: TI-CUBIC is a line fit to the du/dlambda, the reason is that it is off because we don’t have enough states to fit accurately.

## Slide 55
Ne Solvation Free Energy: 10 States

## Slide 56: Task 3: Setting up the free energy parameter in GOMC
Go to freeEnergy/AR/.
Open the “prod.conf” with a text editor and replace the “Fill-by-user” with correct value or values in the following directories.
  states/state_0/.
  states/state_1/.
  states/state_2/.
  states/state_3/.
FreeEnergyCalc true 1000
MoleculeType AR 1
ScalePower 2
ScaleAlpha 0.5
MinSigma 3.0
InitialState Fill-by-user
LambdaVDW Fill-by-user
Define the VDW lambda vector as: 0.00, 0.14, 0.45, 1.00
Set the initial state number for each simulation.
Notes: They must define the VDW lambda and set the initial state to run the NVT simulation at this lambda

## Slide 57: Task 3: Setting up the free energy parameter in GOMC
  state_0/prod.conf
FreeEnergyCalc true 1000
MoleculeType AR 1
ScalePower 2
ScaleAlpha 0.5
InitialState 0
LambdaVDW 0.00 0.14 0.45 1.00
Here is the correct changes to the “prod.conf” file for each simulation:
  states/state_2/prod.conf
FreeEnergyCalc true 1000
MoleculeType AR 1
ScalePower 2
ScaleAlpha 0.5
InitialState 1
LambdaVDW 0.00 0.14 0.45 1.00
FreeEnergyCalc true 1000
MoleculeType AR 1
ScalePower 2
ScaleAlpha 0.5
InitialState 2
LambdaVDW 0.00 0.14 0.45 1.00
FreeEnergyCalc true 1000
MoleculeType AR 1
ScalePower 2
ScaleAlpha 0.5
InitialState 3
LambdaVDW 0.00 0.14 0.45 1.00
  states/state_3/prod.conf
  state_1/prod.conf

## Slide 58: Task 4: Analysis the GOMC free energy outputs.
Run the NVT simulation at 4 intermediate states. (Follow the README.txt)
Go to freeEnergy/AR/result/.
Copy the free energy files into "data" directory
  “cp ../states/state*/Free_Energy_BOX_0_PRODUCTION_*.dat ./data/.”
Calculate the solvation free energy with alchemlyb library
  “python ./free_energy_calc.py”
Plot the solvation free energy with alchemical_analysis tool
  “alchemical_analysis -a gomc -d data -p Free_Energy_BOX_0_PRODUCTION_ -q dat -g True -w True -f 10 -u 'kcal' -o plots -m '-DEXP-IEXP’ ”
Notes: Tell them that they can copy and paste the command from README.txt file

## Slide 59
Ar Solvation Free Energy: 4 States
Notes: TI-CUBIC is a line fit to the du/dlambda, the reason is that it is off because we don’t have enough states to fit accurately.

## Slide 60
Ar Solvation Free Energy: 10 States

## Slide 61: GOMC on Multicore and GPU

## Slide 62: Acknowledgements
Jason Mick, Younes Nejahi, Kamel Rushaidat, Niloofar Torabi, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, OAC-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU