## Slide 1
Hands-On With Monte Carlo Simulations
Mohammad Soroush Barhaghi†, Younes Nejahi‡, Loren Schwiebert‡, and Jeffrey Potoff†
† Department of Chemical Engineering & Materials Science, College of Engineering,
‡ Department of Computer Science, College of Engineering, Wayne State University, Detroit, MI,
USA 48202
Notes: 1- MC simulation engine
2- Developed by potoff group & schwibert
3- Developed for running on CPU and GPU
4- CPU system size < 10,000
5- GPU system size > 10,000

## Slide 2: Tutorial files
On GitHub
Git clone https://github.com/ GOMC-WSU /Workshop.git
Website https://github.com/GOMC-WSU/Workshop
To run example: change the directory to ~/GOMC-Workshop/

## Slide 3: Overview
Grand canonical Monte Carlo simulation
  Adsorption of Ar and CO2 in IRMOF-1
    System setup for adsorption in porous materials, using automated HTS tools
    Extract the simulation results
Canonical Monte Carlo simulation.
  Solvation free energy of Ne, Ar, and Kr in cyclohexane
    System setup for free energy calculation
    Calculate the solvation free energy with TI and FEP estimators

## Slide 4: Acknowledgements
Jason Mick, Younes Nejahi, Kamel Rushaidat, Niloofar Torabi, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, OAC-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU

## Slide 5: Introduction to GOMC

## Slide 6
NVT, NPT, GCMC,
and GEMC
Linear, Branched, cyclic, and Polar molecules
Martini
Charmm
OPLS
Mie
Exp-6
CPU
OpenMP
GPU
OpenMP + GPU
Parallelization
Moves Supported:
Displacement
Rotation
Swap; Intra-swap (CD-CBMC)
Regrowth (CD-CBMC)
MEMC (inter/intra)
Multi-particle move
Free energy calculations
Volume (isotropic, anisotropic)

## Slide 7: GOMC I/O
PDB
PSF
Parameter
Control
Log
PDB
PSF
Block Averages
GCMC: Histogram

## Slide 8: GOMC I/O: Input
PDB
PSF
Parameter
Control
Coordinates of all atoms
Connectivity between atoms and partial charges.
Maps atom names to atom types
Bonded and non-bonded parameters for all atoms,
bonds, angles and dihedrals
Simulation run conditions: box size, temperature
Move ratios, parameter files, etc.

## Slide 9: Single PDB file
ATOM 1 H1 SPCE 1 4.665 10.828 11.349 0.00 0.00
ATOM 2 O1 SPCE 1 4.365 11.775 11.228 0.00 0.00
ATOM 3 H2 SPCE 1 4.473 12.272 12.089 0.00 0.00
END
Atom ID
Atom name
residue name
Residue ID
X, Y, Z coordinates
Occupancy
Beta

## Slide 10: Topology file
RESI SPCE 0.00
GROUP
ATOM O1 OT -0.847600 ! O1
ATOM H1 HT 0.423800 ! / \
ATOM H2 HT 0.423800 ! H1 H2
BOND O1 H1 O1 H2
PATCHING FIRS NONE LAST NONE
Defines residue name
Maps atom name to atom type
Column 3 is the partial charge
Defines bonds between pairs of atoms.
Atom type
Atom name
Partial charges

## Slide 11: GOMC I/O: LOG Output
MOVE_<box number>: move statistics
ENER_<box number>: energies
STAT_<box number>: density
Data are stored in columns, making them straightforward to extract with awk.
Quantities are instantaneous values, and are defined with MTITLE, ETITLE and STITLE headers near the beginning of the log file.
Notes: Talk about output file when Production is running!

## Slide 12: GOMC I/O: LOG Output
80

## Slide 13: GOMC I/O: BLOCK Output

## Slide 14: Grand Canonical Monte Carlo Example

## Slide 15: Grand Canonical Monte Carlo Example
Create Topology file for adsorbate.
Build PDB and PSF files for adsorbate.
Simulation of CO2 adsorption in IRMOF-1 at 298 K and 1.0 bar.
Calculate the number of CO2 adsorbed.

## Slide 16: Creating PDB for adsorbent:
Beta Value
  Beta = 0: Displace, Rotate, Intra-swap, Swap, regrowth
  Beta = 1: Fix position
  Beta = 2: Displace, Rotate, Intra-swap, regrowth
Tcl script in VMD
Notes: Code uses the PDB values in the PDB to determine if a particular molecule should be moved or not.

## Slide 17: Creating PDB for adsorbent:
Download the crystal structure.
Use VESTA to:
  Extend the unit cell by factor of 2.
  Remove the bonds.
  Export the structure as PDB file.
To generate the PDB file, each atom will be considered its own molecule. Assign resname using atom name.
: : : : : : : :

## Slide 18: Creating PDB for adsorbent:
Use convert script to assign resname and resid based on atom name.
vmd < ./ convert_VESTA_PDB.tcl
To generate the PDB file, each atom will be considered its own molecule. Assign resname using atom name.
: : : : : : : : : : : :
: : : : : : : : : : : :

## Slide 19: IRMOF-1 Topology file:
MASS 1 O 15.999 O
MASS 2 C 12.010 C
MASS 3 H 1.0079 H
MASS 4 ZN 65.3800 ZN
DEFA FIRS none LAST none
AUTOGENERATE ANGLES DIHEDRALS
RESI ZN1 1.333 ! IRMOF-1 - DFT charges
ATOM ZN1 ZN 1.333 !
PATCHING FIRS NONE LAST NONE
RESI H1 0.162 ! IRMOF-1 - DFT charges
ATOM H1 H 0.162 !
PATCHING FIRS NONE LAST NONE
RESI O1 -1.564 ! IRMOF-1 - DFT charges
ATOM O1 O -1.564 !
PATCHING FIRS NONE LAST NONE
RESI O2 -0.641 ! IRMOF-1 - DFT charges
ATOM O2 O -0.641 !
PATCHING FIRS NONE LAST NONE
RESI C1 -0.167 ! IRMOF-1 - DFT charges
ATOM C1 C -0.167 !
PATCHING FIRS NONE LAST NONE
RESI C2 0.558 ! IRMOF-1 - DFT charges
ATOM C2 C 0.558 !
PATCHING FIRS NONE LAST NONE
RESI C3 0.106 ! IRMOF-1 - DFT charges
ATOM C3 C 0.106 !
PATCHING FIRS NONE LAST NONE END

## Slide 20: Creating PSF for adsorbent:
Use build scripts (build_EDUSIF_auto.tcl) to separate each residue type and generate PDB and PSF files.
Set beta value to 1 in PDB by using (setBeta.tcl) script.
To generate the PSF file, separate each residue in each file and use psfgen to generate PSF file.
Execute these commands:
vmd < ./build_EDUSIF_auto.tcl
vmd < ./setBeta.tcl

## Slide 21: Grand Canonical Monte Carlo
Acceptance criteria for molecule swap in Grand Canonical ensemble Monte Carlo (GCMC).
Chemical Potential (K)
Fugacity (bar)

## Slide 22: Control file: GCMC
# INPUT PDB, PSF FILES
Coordinates 0 ../build/base/IRMOF_1_BOX_0.pdb
Coordinates 1 ../build/reservoir/START_BOX_1.pdb
Structure 0 ../build/base/IRMOF_1_BOX_0.psf
Structure 1 ../build/reservoir/START_BOX_1.psf
# MOVE FREQUENCY
DisFreq 0.30
RotFreq 0.30
SwapFreq 0.40
# Chemical Potential/Fugacity
Fugacity CO2 1.0
Fugacity C1 0.0
Fugacity C2 0.0
Fugacity C3 0.0
Fugacity H1 0.0
Fugacity O1 0.0
Fugacity O2 0.0
Fugacity ZN1 0.0
Vector1
Vector2
Vector3
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 36.8140 0.0 0.0
CellBasisVector2 0 18.2583 31.9880 0.0
CellBasisVector3 0 18.2712 10.5596 30.1748
CellBasisVector1 1 50.00 0.00 0.00
CellBasisVector2 1 0.00 50.00 0.00
CellBasisVector3 1 0.00 00.00 50.00
# OutHistSettings
DistName dis
HistName his
RunNumber 1
RunLetter a
SampleFreq 200

## Slide 23: GOMC I/O: GCMC
Extract data using awk
  cat output_AR.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_AR_fluct.dat

## Slide 24: GOMC I/O: GCMC
Extract data using awk
  cat output_AR.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_AR_fluct.dat

## Slide 25: GOMC I/O: GCMC
Extract data using awk
  cat output_CO2.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_CO2_fluct.dat

## Slide 26: GOMC I/O: GCMC
Extract data using awk
  cat output_CO2.log | awk '/STAT_0/ {print $2, $3*$5}' > mol_CO2_fluct.dat

## Slide 27: GOMC on Multicore and GPU

## Slide 28: Acknowledgements
Jason Mick, Younes Nejahi, Kamel Rushaidat, Niloofar Torabi, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, OAC-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU