## Slide 1
Hands-On With Monte Carlo Simulations
Mohammad Soroush Barhaghi†, Younes Nejahi‡, Loren Schwiebert‡, and Jeffrey Potoff†
† Department of Chemical Engineering & Materials Science, College of Engineering,
‡ Department of Computer Science, College of Engineering, Wayne State University, Detroit, MI,
USA 48202
Notes: 1- MC simulation engine
2- Developed by potoff group & schwibert
3- Developed for running on CPU and GPU
4- CPU system size < 10,000
5- GPU system size > 10,000

## Slide 2: Tutorial files
On GitHub
Git clone https://github.com/ GOMC-WSU /Workshop.git
Website https://github.com/GOMC-WSU/Workshop
To run example: copy GOMC_CPU_NVT from GOMC/bin to Workshop/NPT/SPCE/

## Slide 3: Overview
NVT and NPT simulations of SPC/E water
  File I/O, basic data analysis, g(r) calculation, visualization
Gibbs ensemble Monte Carlo simulations of methyl-cyclohexane
  Vapor-liquid equilibria, tips and tricks
Grand canonical Monte Carlo simulations of CO2 adsorption in IRMOF-1
  System setup for adsorption in porous materials.

## Slide 4: Acknowledgements
Jason Mick, Younes Nejahi, Kamel Rushaidat, Niloofar Torabi, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, OAC-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU

## Slide 5: Introduction to GOMC

## Slide 6
NVT, NPT,
GCMC, and GEMC
Linear, Branched,
Polar
CPU
OpenMP
GPU
OpenMP + GPU
Parallelization
Martini
Charmm
OPLS
Mie
Custom Potential
Moves Supported:
Displacement
Rotation
Swap (CD-CBMC)
Intra-Swap (CD-CBMC)
Regrowth (CD-CBMC)
MEMC
Intra-MEMC
CrankShaft
Volume:
  Const. Ratio
  Const. Area

## Slide 7: GOMC I/O
PDB
PSF
Parameter
Control
Log
PDB
PSF
Block Averages
GCMC: Histogram

## Slide 8: GOMC I/O: Input
PDB
PSF
Parameter
Control
Coordinates of all atoms
Connectivity between atoms and partial charges.
Maps atom names to atom types
Bonded and non-bonded parameters for all atoms,
bonds, angles and dihedrals
Simulation run conditions: box size, temperature
Move ratios, parameter files, etc.

## Slide 9: NPT Monte Carlo Example
Create Topology and Parameter files.
Build PDB and PSF files.
Equilibrate the SPC/E water at 300 K using NVT ensemble.
Simulation of SPC/E water at 300 K and 1.0 bar, using equilibrated system.
Use the example files to run simulation to calculate the average energy and radial distribution function.

## Slide 10: Building new molecules
Need atomic coordinates of the molecule of interest in PDB format (provided).
Entry in topology file defining bonds between atoms, map of atom names to atom types, and partial charges.
PDB
Topology
PDB-all, PSF
Packmol
PSFGEN

## Slide 11: Single PDB file
ATOM 1 H1 SPCE 1 4.665 10.828 11.349 0.00 0.00
ATOM 2 O1 SPCE 1 4.365 11.775 11.228 0.00 0.00
ATOM 3 H2 SPCE 1 4.473 12.272 12.089 0.00 0.00
END
Atom ID
Atom name
residue name
Residue ID
X, Y, Z coordinates
Occupancy
Beta

## Slide 12: Topology file
RESI SPCE 0.00
GROUP
ATOM O1 OT -0.847600 ! O1
ATOM H1 HT 0.423800 ! / \
ATOM H2 HT 0.423800 ! H1 H2
BOND O1 H1 O1 H2
PATCHING FIRS NONE LAST NONE
Defines residue name
Maps atom name to atom type
Column 3 is the partial charge
Defines bonds between pairs of atoms.
Atom type
Atom name
Partial charges

## Slide 13: Parameter file: Bonds
BONDS
!
!V(bond) = Kb(b - b0)**2
!
!atom type Kb(K/mole/A**2) b0 (A) description
OT HT 9999999999 1.000 ! Fixed.
BONDS
!
!V(bond) = Kb(b - b0)**2
!
!atom type Kb(Kcal/mol /A**2) b0 (A) description
OT HT 9999999999 1.000 ! Fixed.
EXOTIC
CHARMM
Notes: This is redundant. Just have one force field entry, since they are both the same. Put bonds and angles on the same slide. This is a lot of text to expect people will notice the units are different.

## Slide 14: Parameter file: Angles
ANGLES
!
!V(angle) = Ktheta(Theta - Theta0)**2!
!
!atom types Ktheta(K/mole/rad**2) Theta0(degree)
HT OT HT 9999999999 109.50 ! fixed
EXOTIC
CHARMM
ANGLES
!
!V(angle) = Ktheta(Theta - Theta0)**2!
!
!atom types Ktheta(Kcal/mole/rad**2) Theta0(degree)
HT OT HT 9999999999 109.50 !fixed
Notes: Merge with slide 13.

## Slide 15: Parameter file: Dihedrals
DIHEDRALS
!
! V(dihedral) = Kchi(1 + cos(n(chi) - delta))
!
!atom types Kchi(K/mole) n delta(degree)
X CH2 CH2 X 0.000000 0 0.0 !
X CH2 CH2 X 355.029964 1 0.0 !
X CH2 CH2 X -68.189775 2 180.0 !
X CH2 CH2 X 791.317812 3 0.0 !
Notes: Only need one type here, since they are identical.

## Slide 16: Parameter file: Nonbonded
EXOTIC
NONBONDED_MIE
!
! V(mie) = 4*eps*((sig_ij/r_ij)**n-(sig_ij/r_ij)**6)
!
!atom type eps(K) sigma(A) n eps,1-4(K) sigma,1-4(A) n,1-4 !description
OT 78.2054 3.167 12 0.00 0.000 0 ! SPCE
HT 0.0000 0.000 12 0.00 0.000 0 ! SPCE

## Slide 17: Parameter file: Nonbonded
CHARMM
NONBONDED
!
! V(LJ) = eps,i,j[(Rmin,i,j/ri,j)**12 - 2(Rmin,i,j/ri,j)**6]
!
!atom type ignored eps(Kcal/mol) Rmin/2(A) ignored eps,1-4(Kcal/mol) Rmin/2,1-4(A) !description
OT 0.0 -0.15541 1.7774185 0.0 0.00 0.00 ! SPCE
HT 0.0 0.00000 0.0000000 0.0 0.00 0.00 ! SPCE
Notes: Increase font size to 20 or 24.

## Slide 18: Parameter file: Nonbonded Fix (adsorbates)
EXOTIC
NBFIX_MIE
!
! V(mie) = 4*eps*((sig_ij/r_ij)**n-(sig_ij/r_ij)**6)
!
!type1 type2 eps(K) sigma(A) n eps,1-4(K) sigma,1-4(A) n,1-4 !description
C C 0.00 0.000 0 0.00 0.000 0 !
C H 0.00 0.000 0 0.00 0.000 0 !
C O 0.00 0.000 0 0.00 0.000 0 !
C ZN 0.00 0.000 0 0.00 0.000 0 !

## Slide 19: Parameter file: Nonbonded Fix (adsorbates)
CHARMM
NBFIX
!
! V(LJ) = Eps,i,j[(Rmin,i,j/ri,j)**12 - 2(Rmin,i,j/ri,j)**6]
!
! type1 type2 ignored eps(Kcal/mol) Rmin(A) ignored eps,1-4(Kcal/mol) Rmin,1-4(A) !description
C C 0.0 0.000 0.000 0.0 0.00 0.00 !
C H 0.0 0.000 0.000 0.0 0.00 0.00 !
C O 0.0 0.000 0.000 0.0 0.00 0.00 !
C ZN 0.0 0.000 0.000 0.0 0.00 0.00 !
NOTE: CHARMM uses Rmin rather than Rmin/2

## Slide 20: Build initial PDB configuration
tolerance 2.7
filetype pdb
output packed_water.pdb
Structure ./singleMolecule/SPCE.pdb
number 250
inside cube 0.1 0.1 0.1 19.0
end structure
300 K, 0.935 g/cm3 (liquid density); 250 molecules -> L=20.0 A
Execute this command:
./packmol <pack_box_0.inp

## Slide 21: Build PSF
psfgen<<ENDMOL
topology ./top_SPCE_water.inp
segment SPCE {
pdb ./packed_water.pdb
auto angles dihedrals
first none
last none
}
Coordpdb ./packed_water.pdb SPCE
Writepsf ./START_BOX_0.psf
writepdb ./START_BOX_0.pdb
SPC/E Water
Execute this command:
vmd < ./build_psf_box_0.tcl
Notes: Auto angles dihedrals tells psfgen to automatically generate the required angle and dihedral information.

## Slide 22: Control file
Restart false
# FORCE FIELD
ParaTypeCHARMM true
Parameters ./par_SPCE_Charmm.par
# INPUT PDB
Coordinates 0 ./../build/START_BOX_0.pdb
# INPUT PSF
Structure 0 ./../build/START_BOX_0.psf
# MOVE FREQUENCY
DisFreq 0.50
RotFreq 0.40
RegrowthFreq 0.10
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 20.00 0.00 0.00
CellBasisVector2 0 0.00 20.00 0.00
CellBasisVector3 0 0.00 0.00 20.00
Restart true
# FORCE FIELD
ParaTypeCHARMM true
Parameters ./par_SPCE_Charmm.par
# INPUT PDB
Coordinates 0 ./../Equilibration/SPCE_EQ_BOX_0_restart.pdb
# INPUT PSF
Structure 0 ./../Equilibration/SPCE_EQ_merged.psf
# MOVE FREQUENCY
DisFreq 0.50
RotFreq 0.49
VolFreq 0.01
# BOX DIMENSION #, X, Y, Z
# CellBasisVector1 0 20.00 0.00 0.00
# CellBasisVector2 0 0.00 20.00 0.00
# CellBasisVector3 0 0.00 0.00 20.00
eq.conf
prod.conf

## Slide 23: GOMC I/O: LOG Output
MOVE_<box number>: move statistics
ENER_<box number>: energies
STAT_<box number>: density
Data are stored in columns, making them straightforward to extract with awk.
Quantities are instantaneous values, and are defined with MTITLE, ETITLE and STITLE headers near the beginning of the log file.
Notes: Talk about output file when Production is running!

## Slide 24: GOMC I/O: LOG Output
80

## Slide 25: GOMC I/O: BLOCK Output

## Slide 26: GOMC I/O: Output
Extract data using awk
  awk ‘/ENER_0/ {print $2, $3}’ output_water.log > energy.dat
  grep “ENER_0” output_water.log | awk ‘{print $2, $3}’ > energy.dat
Notes: Add pressure vs MCS to this slide.

## Slide 27: GOMC: RDF
Follow README.txt to generate RDF
OT - OT

## Slide 28: Gibbs Ensemble Monte Carlo
Volume Exchange
Particle Displacement
Molecule Transfer
Bulk liquid and vapor
External (NVT): NT, VT, T are constant Chemical equilibrium: μL= μV
Mechanical Equilibrium: PV=PL

## Slide 29: GEMC Example
Workshop/NVT_GEMC/methylCyclohexane
Need to build initial configurations for two boxes.
Issuing the following commands to create START_BOX_*.pdb, *.psf
./packmol <pack_box_0.inp
./packmol <pack_box_1.inp
./build_psf_box_0.tcl or try vmd < build_psf_box_0.tcl
./build_psf_box_1.tcl or try vmd < build_psf_box_1.tcl
Could be combined into a single shell script.

## Slide 30: GEMC Control File
# INPUT PDB, PSF FILES
Coordinates 0 ../build/START_BOX_0.pdb
Coordinates 1 ../build/START_BOX_1.pdb
Structure 0 ../build/START_BOX_0.psf
Structure 1 ../build/START_BOX_1.psf
# GEMC TYPE
GEMC NVT
# PRESSURE CALC
PressureCalc true 1000
# MOVE FREQUENCY
DisFreq 0.30
RotFreq 0.28
RegrowthFreq 0.10
CrankShaftFreq 0.10
SwapFreq 0.20
VolFreq 0.02
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 55.00 0.0 0.0
CellBasisVector2 0 0.00 55.00 0.0
CellBasisVector3 0 0.00 0.00 55.00
CellBasisVector1 1 73.00 0.00 0.00
CellBasisVector2 1 0.00 73.00 0.00
CellBasisVector3 1 0.00 00.00 73.00
# CBMC TRIALS
CBMC_First 8
CBMC_Nth 4
CBMC_Ang 100
CBMC_Dih 10
# OUTPUT FREQUENCY
CoordinatesFreq true 10000
RestartFreq true 500000
ConsoleFreq true 10000
BlockAverageFreq true 10000
# OUTPUT BLK. FLUC.
OutEnergy true true
OutPressure true true
OutMolNum true true
OutDensity true true
OutVolume true true
Notes: Run the simulation and then start talking about CBMC

## Slide 31: Configurational-Bias Monte Carlo
Generate a number (n) of random trial positions in the target box, calculate a (new) insertion Rosenbluth weight based on the Boltzmann factors of the trial insertion sites:
Select a site using a random draw compared to the scaled Boltzmann factors for each site:
-trial position
-winner position

## Slide 32: Configurational-Bias Monte Carlo
Generate independent and dependent angle trials, while keeping the angle in the ring fixed:
Martin and Siepmann, J. Phys. Chem B, 103, 4508 (1999)
=
For n sites grown off a branch point ngrow(n)=n-1
These angles ([a]) are fully independent from a spatial perspective
These angles ([b]) are spatially dependent on the picks from [a].
Fixed
Flexible
Flexible

## Slide 33: Configurational-Bias Monte Carlo
Martin and Siepmann, J. Phys. Chem B, 103, 4508 (1999)
Generate a number (m) of random trial orientation around focus atom, calculate a (new) Rosenbluth weight based on the Boltzmann factors of the trial insertion sites:

## Slide 34: Configurational-Bias Monte Carlo
Martin and Siepmann, J. Phys. Chem B, 103, 4508 (1999)
Select a orientation using a random draw compared to the scaled Boltzmann factors for each site:

## Slide 35: Configurational-Bias Monte Carlo
Martin and Siepmann, J. Phys. Chem B, 103, 4508 (1999)
Continue building the molecule segment by segment. If building segment is in the ring frame, we do not perform dihedral trials.
Torsion is coupled to nonbonded energy
Picking for bond angle is decoupled.
# of growth steps where each step regrows all segments from a branch point

## Slide 36: Configurational-Bias CrankShaft

## Slide 37: GEMC: methyl-cyclohexane 480 K
Exclude first 500,000 MCS from block average files.
,

## Slide 38: GEMC: methyl-cyclohexane 480 K
Start from 250 molecules and L=53 A
for each box.
As long as one starts in the two phase region, GEMC will form two distinct phases.
Gas
Liquid
Gas
Liquid

## Slide 39: GEMC Tips
Choice of simulation parameters may effect length of equilibration required.
Number of molecules in each phase also effects the magnitude of the statistical uncertainties.
Larger volume = more molecules in gas phase.

## Slide 40: GEMC PDB Output
PDB output files for each box contain coordinates for all molecules in the simulation: mC6cycle_GEMC_T_480K_BOX_0.pdb
The occupancy column is used to designate the box to which each molecule belongs. “imaginary” molecules are given coordinates of 0,0,0.
  ATOM 76 C6 1C6 A 11 33.658 11.434 28.090 0.00 0.00
  ATOM 77 C7 1C6 A 11 36.151 10.979 27.972 0.00 0.00
  ATOM 78 C1 1C6 A 12 0.000 0.000 0.000 1.00 0.00
Notes: Need to include an image of each equilibrated box.

## Slide 41: GEMC methyl-cyclohexane
Notes: Please add a citation to the literature for the Yianno…data.

## Slide 42: Grand Canonical Monte Carlo Example

## Slide 43: Grand Canonical Monte Carlo Example
Create Topology file for adsorbate.
Build PDB and PSF files for adsorbate.
Simulation of CO2 adsorption in IRMOF-1 at 298 K and 1.0 bar.
Calculate the number of CO2 adsorbed.

## Slide 44: Creating PDB for adsorbent:
Beta Value
  Beta = 0: Displace, Rotate, Intra-swap, Swap, regrowth
  Beta = 1: Fix position
  Beta = 2: Displace, Rotate, Intra-swap, regrowth
Tcl script in VMD
Notes: Code uses the PDB values in the PDB to determine if a particular molecule should be moved or not.

## Slide 45: Creating PDB for adsorbent:
Download the crystal structure.
Use VESTA to:
  Extend the unit cell by factor of 2.
  Remove the bonds.
  Export the structure as PDB file.
To generate the PDB file, each atom will be considered its own molecule. Assign resname using atom name.
: : : : : : : :

## Slide 46: Creating PDB for adsorbent:
Use convert script to assign resname and resid based on atom name.
vmd < ./ convert_VESTA_PDB.tcl
To generate the PDB file, each atom will be considered its own molecule. Assign resname using atom name.
: : : : : : : : : : : :
: : : : : : : : : : : :

## Slide 47: IRMOF-1 Topology file:
MASS 1 O 15.999 O
MASS 2 C 12.010 C
MASS 3 H 1.0079 H
MASS 4 ZN 65.3800 ZN
DEFA FIRS none LAST none
AUTOGENERATE ANGLES DIHEDRALS
RESI ZN1 1.333 ! IRMOF-1 - DFT charges
ATOM ZN1 ZN 1.333 !
PATCHING FIRS NONE LAST NONE
RESI H1 0.162 ! IRMOF-1 - DFT charges
ATOM H1 H 0.162 !
PATCHING FIRS NONE LAST NONE
RESI O1 -1.564 ! IRMOF-1 - DFT charges
ATOM O1 O -1.564 !
PATCHING FIRS NONE LAST NONE
RESI O2 -0.641 ! IRMOF-1 - DFT charges
ATOM O2 O -0.641 !
PATCHING FIRS NONE LAST NONE
RESI C1 -0.167 ! IRMOF-1 - DFT charges
ATOM C1 C -0.167 !
PATCHING FIRS NONE LAST NONE
RESI C2 0.558 ! IRMOF-1 - DFT charges
ATOM C2 C 0.558 !
PATCHING FIRS NONE LAST NONE
RESI C3 0.106 ! IRMOF-1 - DFT charges
ATOM C3 C 0.106 !
PATCHING FIRS NONE LAST NONE END

## Slide 48: Creating PSF for adsorbent:
Use build scripts (build_EDUSIF_auto.tcl) to separate each residue type and generate PDB and PSF files.
Set beta value to 1 in PDB by using (setBeta.tcl) script.
To generate the PSF file, separate each residue in each file and use psfgen to generate PSF file.
Execute these commands:
vmd < ./build_EDUSIF_auto.tcl
vmd < ./setBeta.tcl

## Slide 49: Grand Canonical Monte Carlo
Acceptance criteria for molecule swap in Grand Canonical ensemble Monte Carlo (GCMC).
Chemical Potential (K)
Fugacity (bar)

## Slide 50: Control file: GCMC
# INPUT PDB, PSF FILES
Coordinates 0 ../build/base/IRMOF_1_BOX_0.pdb
Coordinates 1 ../build/reservoir/START_BOX_1.pdb
Structure 0 ../build/base/IRMOF_1_BOX_0.psf
Structure 1 ../build/reservoir/START_BOX_1.psf
# MOVE FREQUENCY
DisFreq 0.30
RotFreq 0.30
SwapFreq 0.40
# Chemical Potential/Fugacity
Fugacity CO2 1.0
Fugacity C1 0.0
Fugacity C2 0.0
Fugacity C3 0.0
Fugacity H1 0.0
Fugacity O1 0.0
Fugacity O2 0.0
Fugacity ZN1 0.0
Vector1
Vector2
Vector3
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 36.8140 0.0 0.0
CellBasisVector2 0 18.2583 31.9880 0.0
CellBasisVector3 0 18.2712 10.5596 30.1748
CellBasisVector1 1 50.00 0.00 0.00
CellBasisVector2 1 0.00 50.00 0.00
CellBasisVector3 1 0.00 00.00 50.00
# OutHistSettings
DistName dis
HistName his
RunNumber 1
RunLetter a
SampleFreq 200

## Slide 51: GOMC I/O: GCMC
Extract data using awk
  cat Blk_CO2_IRMOF_1_BOX_0.dat | awk '{print $1, $10 * $19}' > mol_CO2.dat
Notes: Molecule should be “molecules”; “probability of distribution” should be P(N).

## Slide 52: GOMC on Multicore and GPU

## Slide 53: Acknowledgements
Jason Mick, Younes Nejahi, Kamel Rushaidat, Niloofar Torabi, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, OAC-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU