## Slide 1
Hands-On With Monte Carlo Simulations
Mohammad Soroush Barhaghi†, Younes Nejahi‡, Loren Schwiebert‡, and Jeffrey Potoff†
† Department of Chemical Engineering & Materials Science, College of Engineering,
‡ Department of Computer Science, College of Engineering, Wayne State University, Detroit, MI,
USA 48202
Notes: 1- MC simulation engine
2- Developed by potoff group & schwibert
3- Developed for running on CPU and GPU
4- CPU system size < 10,000
5- GPU system size > 10,000

## Slide 2: Tutorial files
On GitHub
Git clone https://github.com/ GOMC-WSU /Workshop.git
Website https://github.com/GOMC-WSU/Workshop
To run example: copy GOMC_CPU_NVT from GOMC/bin to Workshop/NPT/SPCE/

## Slide 3: Acknowledgements
Mohammad Soroush Barhaghi, Jason Mick, Younes Nejahi, Kamel Rushaidat, Runxuan Jiang, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, ACI-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU

## Slide 4: Configurational-Bias Monte Carlo
Generate a number (k) of random trial positions in the target box, calculate a (new) insertion Rosenbluth weight based on the Boltzmann factors of the trial insertion sites:
Select a site using a random draw compared to the scaled Boltzmann factors for each site:
Generate random trial positions in the losing box (k-1), calculate old Rosenbluth weight based on the Boltzmann factors of those positions in the losing box, plus the actual position.
Accept the insertion if
Trial insertion
Existing molecules

## Slide 5: Coupled-Decoupled Configurational Bias
Torsion is coupled to nonbonded energy
Picking for bond angle is decoupled.
# of growth steps
where each step regrows all segments from a branch point
=
For n sites grown off a branch point ngrow(n)=n-1
These angles ([a]) are fully independent from a spatial perspective
These angles ([b]) are spatially dependent on the picks from [a].
i1
p
b1
f
a1
a2
i2
i3
t
Martin and Siepmann, J. Phys. Chem B, 103, 4508 (1999)

## Slide 6: Introduction to GOMC

## Slide 7
NVT, NPT,
GCMC, and GEMC
Linear, Branched,
Polar
CPU
OpenMP
GPU
OpenMP + GPU
Parallelization
Martini
Charmm
OPLS
Mie
Custom Potential
Moves Supported:
Displacement
Rotation
Swap (CD-CBMC)
Intra-Swap (CD-CBMC)
Regrowth (CD-CBMC)
MEMC
Intra-MEMC
CrankShaft
Volume:
  Const. Ratio
  Const. Area

## Slide 8: GOMC I/O
PDB
PSF
Parameter
Control
Log
PDB
PSF
Block Averages
GCMC: Histogram

## Slide 9: GOMC I/O: Input
PDB
PSF
Parameter
Control
Coordinates of all atoms
Connectivity between atoms and partial charges.
Maps atom names to atom types
Bonded and non-bonded parameters for all atoms,
bonds, angles and dihedrals
Simulation run conditions: box size, temperature
Move ratios, parameter files, etc.

## Slide 10: GOMC I/O: Output
MOVE_<box number>: move statistics
ENER_<box number>: energies
STAT_<box number>: density
Data are stored in columns, making them straightforward to extract with awk.
Quantities instantaneous values, and are defined with MTITLE, ETITLE and STITLE headers near the beginning of the log file.

## Slide 11: NVT Monte Carlo Example
Simulation of argon at 120 K and at saturated liquid density.
Use the example files to run simulation to calculate the average energy and radial distribution function.
Next step: Build input files for n-butane and rerun the simulation at 300 K and 0.567 g/cm3.

## Slide 12: GOMC I/O: Output
Extract data using awk
  awk ‘/ENER_0/ {print $2, $3}’ argon_120.log > energy.dat
  grep “ENER_0” argon_120.log | awk {print $2, $3}’ > energy.dat

## Slide 13: GOMC: RDF
package require pbctools
#load PDB and set box size
mol new Argon_NVT_T_120K_BOX_0.pdb waitfor all
pbc set {38.527 38.527 38.527}
set nframes [molinfo top get numframes]
set sel1 [atomselect top "resname AR"]
set sel2 [atomselect top "resname AR"]
#calculate RDF on multicore
set rdf [measure gofr $sel1 $sel2 delta 0.01
rmax 14.0 usepbc 1 selupdate 0 first 0 last
[expr {$nframes-1}] step 1]
#organize data for printing
set ri [lindex $rdf 0]
set gr [lindex $rdf 1]
set rdf_out [open "rdf.dat" "w"]
foreach val1 $ri val2 $gr {
puts $rdf_out "$val1\t$val2"
}
close $rdf_out
exit

## Slide 14: Using the restart file
#########################
# enable, step
#########################
Restart false
####################################
# INPUT PDB FILES
####################################
Coordinates 0 ../build/START_BOX_0.pdb
####################################
# INPUT PSF FILES
####################################
Structure 0 ../build/START_BOX_0.psf
#########################
# enable, step
#########################
Restart true
####################################
# INPUT PDB FILES
####################################
Coordinates 0 ./Argon_NVT_T_120K_BOX_0_restart.pdb
####################################
# INPUT PSF FILES
####################################
Structure 0 ./Argon_NVT_T_120K_merged.psf

## Slide 15: Using the restart file
Packmol initial configuration
Restart initial configuration
Restart file is very useful for systems where the density fluctuates (GEMC, GCMC).

## Slide 16: Building new molecules
Need atomic coordinates of the molecule of interest in PDB format.
Entry in topology file defining bonds between atoms, map of atom names to atom types, and partial charges.
PDB
Topology
PDB-all, PSF
Packmol
PSFGEN

## Slide 17: Topology file
RESI C4A 0.00 ! n-butane
GROUP
ATOM C1 CH3 0.00 ! C1 C3
ATOM C2 CH2 0.00 ! \ / \
ATOM C3 CH2 0.00 ! C2 C4
ATOM C4 CH3 0.00 !
BOND C1 C2 C2 C3 C3 C4
PATCHING FIRS NONE LAST NONE
Defines residue name
Maps atom name to atom type
Column 3 is the partial charge
Defines bonds between pairs of atoms.

## Slide 18: Parameter file: Bonds
BONDS
!
!V(bond) = Kb(b - b0)**2
!
!atom type Kb(K/mole/A**2) b0 (A) description
CH3 CH3 9999999999 1.540 ! Fixed.
CH3 CH2 9999999999 1.540 ! Fixed.
CH2 CH2 9999999999 1.540 ! Fixed.
BONDS
!
!V(bond) = Kb(b - b0)**2
!
!atom type Kb(Kcal/mol /A**2) b0 (A) description
CH3 CH3 9999999999 1.540 ! Fixed.
CH3 CH2 9999999999 1.540 ! Fixed.
CH2 CH2 9999999999 1.540 ! Fixed.
EXOTIC
CHARMM

## Slide 19: Parameter file: Angles
ANGLES
!
!V(angle) = Ktheta(Theta - Theta0)**2!
!
!atom types Ktheta(K/mole/rad**2) Theta0(degree)
CH3 CH2 CH3 31250 114.00 !
CH3 CH2 CH2 31250 114.00 !
CH2 CH2 CH2 31250 114.00 !
EXOTIC
CHARMM
ANGLES
!
!V(angle) = Ktheta(Theta - Theta0)**2!
!
!atom types Ktheta(Kcal/mole/rad**2) Theta0(degree)
CH3 CH2 CH3 62.10013 114.00 !
CH3 CH2 CH2 62.10013 114.00 !
CH2 CH2 CH2 62.10013 114.00 !

## Slide 20: Parameter file: Dihedrals
DIHEDRALS
!
! V(dihedral) = Kchi(1 + cos(n(chi) - delta))
!
!atom types Kchi(K/mole) n delta(degree)
X CH2 CH2 X 0.000000 0 0.0 !
X CH2 CH2 X 355.029964 1 0.0 !
X CH2 CH2 X -68.189775 2 180.0 !
X CH2 CH2 X 791.317812 3 0.0 !
EXOTIC
CHARMM
DIHEDRALS
!
! V(dihedral) = Kchi(1 + cos(n(chi) - delta))
!
!atom types Kchi(Kcal/mole) n delta(degree)
X CH2 CH2 X 0.000000 0 0.0 !
X CH2 CH2 X 0.705517 1 0.0 !
X CH2 CH2 X -0.135507 2 180.0 !
X CH2 CH2 X 1.572510 3 0.0 !

## Slide 21: Parameter file: Nonbonded
EXOTIC
NONBONDED_MIE
!
! V(mie) = 4*eps*((sig_ij/r_ij)**n-(sig_ij/r_ij)**6)
!
!atom type eps(K) sigma(A) n eps,1-4(K) sigma,1-4(A) n,1-4 !description
CH4 161.00 3.740 14 0.00 0.000 0 ! Mie
CH3 121.25 3.783 16 0.00 0.000 0 ! Mie
CH2 61.00 3.990 16 0.00 0.000 0 ! Mie

## Slide 22: Parameter file: Nonbonded
CHARMM
NONBONDED
!
! V(LJ) = eps,i,j[(Rmin,i,j/ri,j)**12 - 2(Rmin,i,j/ri,j)**6]
!
!atom type ignored eps(Kcal/mol) Rmin/2(A) ignored eps,1-4(Kcal/mol) Rmin/2,1-4(A) !description
CH4 0.0 -0.294106207 2.093391720 0.0 0.00 0.00 ! TraPPE 1
CH3 0.0 -0.194746002 2.104616341 0.0 0.00 0.00 ! TraPPE 1
CH2 0.0 -0.091411389 2.216862545 0.0 0.00 0.00 ! TraPPE 1

## Slide 23: Parameter file: Nonbonded Fix (adsorbates)
EXOTIC
NBFIX_MIE
!
! V(mie) = 4*eps*((sig_ij/r_ij)**n-(sig_ij/r_ij)**6)
!
!type1 type2 eps(K) sigma(A) n eps,1-4(K) sigma,1-4(A) n,1-4 !description
C C 0.00 0.000 0 0.00 0.000 0 !
C H 0.00 0.000 0 0.00 0.000 0 !
C O 0.00 0.000 0 0.00 0.000 0 !
C ZN 0.00 0.000 0 0.00 0.000 0 !

## Slide 24: Parameter file: Nonbonded Fix (adsorbates)
CHARMM
NBFIX
!
! V(LJ) = Eps,i,j[(Rmin,i,j/ri,j)**12 - 2(Rmin,i,j/ri,j)**6]
!
! type1 type2 ignored eps(Kcal/mol) Rmin(A) ignored eps,1-4(Kcal/mol) Rmin,1-4(A) !description
C C 0.0 0.000 0.000 0.0 0.00 0.00 !
C H 0.0 0.000 0.000 0.0 0.00 0.00 !
C O 0.0 0.000 0.000 0.0 0.00 0.00 !
C ZN 0.0 0.000 0.000 0.0 0.00 0.00 !
NOTE: CHARMM uses Rmin rather than Rmin/2

## Slide 25: Build initial configuration
tolerance 3.0
filetype pdb
output packed_argon.pdb
Structure ./singleMolecule/argon.pdb
number 1000
inside cube 0.1 0.1 0.1 37.
end structure
tolerance 3.0
filetype pdb
output packed_butane.pdb
Structure butane_ua2.pdb
number 1000
inside cube 2. 2. 2. 53. 53. 53.
end structure
300 K, 0.5672 g/cm3 (saturated liquid density); 1000 molecules -> L~55.4 A
./packmol <pack_box_0.inp

## Slide 26: Build PSF
psfgen<<ENDMOL
topology ./top_NobleGases.inp
segment AR {
pdb ./packed_argon.pdb
first none
last none
}
coordpdb ./packed_argon.pdb AR
writepsf ./START_BOX_0.psf
writepdb ./START_BOX_0.pdb
psfgen<<ENDMOL
topology ./top_mie.inp
segment C4A {
pdb ./packed_butane.pdb
auto angles dihedrals
first none
last none
}
coordpdb ./packed_butane.pdb C4A
writepsf ./START_BOX_0.psf
writepdb ./START_BOX_0.pdb
Argon
Butane
Notes: Auto angles dihedrals tells psfgen to automatically generate the required angle and dihedral information.

## Slide 27: Modify control file
ParaTypeEXOTIC true
Parameters ./par_NobleGases_Mie.par
# MOVE FREQUENCY
DisFreq 0.90
RotFreq 0.00
IntraSwapFreq 0.10
RegrowthFreq 0.00
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 38.527 0.00 0.00
CellBasisVector2 0 0.00 38.527 0.00
CellBasisVector3 0 0.00 0.00 38.527
# CBMC TRIALS
CBMC_First 8
CBMC_Nth 6
CBMC_Ang 0
CBMC_Dih 0
ParaTypeEXOTIC true
Parameters ./par_mie.inp
# MOVE FREQUENCY
DisFreq 0.60
RotFreq 0.10
IntraSwapFreq 0.10
RegrowthFreq 0.20
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 55.41 0.00 0.00
CellBasisVector2 0 0.00 55.41 0.00
CellBasisVector3 0 0.00 0.00 55.41
# CBMC TRIALS
CBMC_First 8
CBMC_Nth 6
CBMC_Ang 100
CBMC_Dih 100
Argon
Butane
Notes: Auto angles dihedrals tells psfgen to automatically generate the required angle and dihedral information.

## Slide 28: Butane NVT at 300K and 0.567 g/cm3
CH3-CH3 interactions

## Slide 29: Gibbs Ensemble Monte Carlo
Volume Exchange
Particle Displacement
Molecule Transfer
Bulk liquid and vapor
External (NVT): NT, VT, T are constant Chemical equilibrium: μL= μV
Mechanical Equlibrium: PV=PL

## Slide 30: GEMC Example
Workshop/NVT_GEMC
Need to build initial configurations for two boxes.
Issuing the following commands to create START_BOX_*.pdb, *.psf
./packmol <pack_box_0.inp
./packmol <pack_box_1.inp
./build_psf_box_0.tcl or try vmd < build_ps_box_0.tcl
./build_psf_box_1.tcl or try vmd < build_ps_box_1.tcl
Could be combined into a single shell script.

## Slide 31: GEMC: Argon 120 K
Exclude first 500,000 MCS from block average files.
; literature
; literature

## Slide 32: GEMC: Argon 120K
Start from 500 molecules and L=40 A
for each box.
As long as one starts in the two phase region, GEMC will form two distinct phases.
Gas
Liquid
Gas
Liquid

## Slide 33: GEMC Tips
Choice of simulation parameters may effect length of equilibration required.
Number of molecules in each phase also effects the magnitude of the statistical uncertainties.

## Slide 34: GEMC: Restart files
For GEMC, the “merged” PSF file written by GOMC contains the information for both boxes.
####################################
# INPUT PSF FILES
####################################
Structure 0 ../argon_T_120K/Argon_GEMC_T_120K_merged.psf
Structure 1 ../argon_T_120K/Argon_GEMC_T_120K_merged.psf

## Slide 35: GEMC PDB Output
“restart” PDB contains only the coordinates for atoms in that phase.
PDB output files for each box contain coordinates for all molecules in the simulation: Argon_GEMC_T_120K_BOX_0.pdb
The occupancy column is used to designate the box to which each molecule belongs. “imaginary” molecules are given coordinates of 0,0,0.
ATOM 29 AR AR A 29 21.324 0.131 25.770 0.00 0.00
ATOM 30 AR AR A 30 29.973 1.108 36.433 0.00 0.00
ATOM 31 AR AR A 31 0.000 0.000 0.000 1.00 0.00
Unfortunately, VMD does not understand changing the number of molecules in the simulation. VMD also does not update occupancy values.

## Slide 36: GEMC PDB Output
#set selection to ignore all molecules with 0, 0, 0 coordinates.
set AllSel1 [atomselect top "name $sel1 and x != 0.0 and y != 0.0 and z !=0.0" frame $j]
set AllSel2 [atomselect top "name $sel2 and x != 0.0 and y != 0.0 and z !=0.0" frame $j]
set BoxL [lindex $BoxDim 0 $j]
pbc set "$BoxL $BoxL $BoxL“
#calculate RDF
set temRDF [measure gofr $AllSel1 $AllSel2 delta $stepSize rmax $rcut usepbc 1]

## Slide 37: Grand Canonical Monte Carlo
External (μVT): μ, V, T are constant and imposed by reservoir on simulation box. Fluctuating: N, P, and E .

## Slide 38: Grand Canonical Monte Carlo
Acceptance criteria for molecule swap in Grand Canonical ensemble Monte Carlo (GCMC).

## Slide 39: Grand Canonical Monte Carlo
For ideal gas:
For non-ideal gas:

## Slide 40: Creating PDB, PSF for reservoir:
GCMC requires two simulation boxes, one for the reservoir and the other for the adsorbent.
To prepare the reservoir, we use 1000 argon molecules in 40 Å cubic box.
tolerance 3.0
filetype pdb
output packed_argon.pdb
Structure ./singleMolecule/argon.pdb
number 1000
inside cube 0.1 0.1 0.1 38.
end structure
psfgen<<ENDMOL
topology ../topology_EDUSIF.inp
segment AR {
pdb ./packed_argon.pdb
first none
last none
}
coordpdb ./packed_argon.pdb AR
writepsf ./START_BOX_1.psf
writepdb ./START_BOX_1.pdb

## Slide 41: Creating PDB for adsorbent:
Beta Value
  Beta = 0: Displace, Rotate, Intra-swap, Swap, regrowth
  Beta = 1: Fix
  Beta = 2: Displace, Rotate, Intra-swap, regrowth
Tcl script in VMD
Notes: Code uses the PDB values in the PDB to determine if a particular molecule should be moved or not.

## Slide 42: Creating PDB for adsorbent:
Download the crystal structure.
Use VESTA to:
  Extend the unit cell by factor of 2.
  Remove the bonds.
  Export the structure as PDB file.
Use convert script to assign resname and resid based on atom name.
To generate the PDB file, each atom will be considered its own molecule. Assign resname using atom name.

## Slide 43: Building “Base”
vmd < convert_VESTA_PDB.tcl
vmd < build_EDUSIF_auto.tcl
vmd < setBeta.tcl

## Slide 44: Creating PSF for adsorbent:
Use build scripts (convert_VESTA_PDB.tcl, build_EDUSIF_auto.tcl) to separate each residue type and generate PDB files.
Set beta value to 1 in PDB by using setBeta.tcl script.
To generate the PSF file, separate each residue in each file and use psfgen to generate PSF file.

## Slide 45: Creating PSF for adsorbent:
segment O {
pdb O.pdb
first none
last none
}
segment H {
pdb H.pdb
first none
last none
}
coordpdb ZN.pdb Zn
coordpdb C.pdb C
coordpdb O.pdb O
coordpdb H.pdb H
writepsf IRMOF_1_BOX_0.psf
writepdb IRMOF_1_BOX_0.pdb
package require psfgen
topology ../topology_EDUSIF.inp
exec grep -w "Zn" EDUSIF_clean_min_modified.pdb > ZN.pdb
exec grep -w "C" EDUSIF_clean_min_modified.pdb > C.pdb
exec grep -w "O" EDUSIF_clean_min_modified.pdb > O.pdb
exec grep -w "H" EDUSIF_clean_min_modified.pdb > H.pdb
segment Zn {
pdb ZN.pdb
first none
last none
}
segment C {
pdb C.pdb
first none
last none
}

## Slide 46: IRMOF-1 Topology file:
MASS 1 O 15.999 O !
MASS 2 C 12.0107 C !
MASS 3 H 1.00794 H !
MASS 4 ZN 65.38 ZN !
MASS 5 AR 39.948 AR !
DEFA FIRS none LAST none
AUTOGENERATE ANGLES DIHEDRALS
RESI C 0.000
GROUP
ATOM C C 0.000
PATCHING FIRS NONE LAST NONE
RESI H 0.000
GROUP
ATOM H H 0.000
PATCHING FIRS NONE LAST NONE
RESI O 0.000
GROUP
ATOM O O 0.000
PATCHING FIRS NONE LAST NONE
RESI Zn 0.000
GROUP
ATOM Zn ZN 0.000
PATCHING FIRS NONE LAST NONE
RESI AR 0.00 ! argon
GROUP
ATOM AR AR 0.00 ! *
PATCHING FIRS NONE LAST NONE
END

## Slide 47: Control file: GCMC
ParaTypeEXOTIC true
Parameters ./par_IRMOF_NobleGases_Mie.par
# INPUT PDB, PSF FILES
Coordinates 0 ../build/base/IRMOF_1_BOX_0.pdb
Coordinates 1 ../build/reservoir/START_BOX_1.pdb
Structure 0 ../build/base/IRMOF_1_BOX_0.psf
Structure 1 ../build/reservoir/START_BOX_1.psf
# MOVE FREQUENCY
DisFreq 0.20
RotFreq 0.00
IntraSwapFreq 0.20
RegrowthFreq 0.0
SwapFreq 0.60
# Chemical Potential/Fugacity
Fugacity AR 5.0
Fugacity C 0
Fugacity H 0
Fugacity O 0
Fugacity ZN 0
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 36.8140 0.0 0.0
CellBasisVector2 0 18.2583 31.9880 0.0
CellBasisVector3 0 18.2712 10.5596 30.1748
CellBasisVector1 1 40.00 0.00 0.00
CellBasisVector2 1 0.00 40.00 0.00
CellBasisVector3 1 0.00 00.00 40.00
# OutHistSettings
DistName dis
HistName his
RunNumber 1
RunLetter a
SampleFreq 200
Vector1
Vector2
Vector3

## Slide 48: Argon Adsorption in IRMOF-1

## Slide 49: NPT-GEMC Example
The Gibbs ensemble method can be used to compute adsorption isotherms in nanoporous materials. One of the boxes contains the framework, while the other box contains the fluid phase (either gas or liquid) that is in equilibrium with the adsorbed phase. The fluid-phase box is maintained at constant pressure (and temperature) by applying volume moves

## Slide 50: Comparing control files:
# GEMC TYPE (DEFULT IS NVT_GEMC)
GEMC NPT
Pressure 5.0
FixVolBox0 true
# MOVE FREQUENCY
DisFreq 0.48
RotFreq 0.00
IntraSwapFreq 0.20
SwapFreq 0.30
VolFreq 0.02
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 36.8140 0.0 0.0
CellBasisVector2 0 18.2583 31.9880 0.0
CellBasisVector3 0 18.2712 10.5596 30.1748
CellBasisVector1 1 103.00 0.00 0.00
CellBasisVector2 1 0.00 103.00 0.00
CellBasisVector3 1 0.00 00.00 103.00
NPT-GEMC
# GEMC TYPE (DEFULT IS NVT_GEMC)
GEMC NVT
# MOVE FREQUENCY
DisFreq 0.68
RotFreq 0.00
IntraSwapFreq 0.10
SwapFreq 0.20
VolFreq 0.02
# BOX DIMENSION #, X, Y, Z
CellBasisVector1 0 37.00 0.00 0.00
CellBasisVector2 0 0.00 37.00 0.00
CellBasisVector3 0 0.00 0.00 37.00
CellBasisVector1 1 58.00 0.00 0.00
CellBasisVector2 1 0.00 58.00 0.00
CellBasisVector3 1 0.00 0.00 58.00
NVT-GEMC

## Slide 51: Histogram Methods
The constant is determined by extrapolating the predicted partition function to very low densities, where the system exhibits ideal gas behavior.
Locate coexistence by varying until equal area is obtained under each peak of the distribution.

## Slide 52: One component VLE from histograms
Find the “bridge” between phases near the critical point.
Run gas phase simulations to determine the constant in
Predict VLE, use reweighted data to determine the run conditions for the next simulations.

## Slide 53: GOMC on Multicore and GPU

## Slide 54: GOMC on multicore CPUs
If you have openMP installed, on Linux GOMC will autodetect and compile with support for multicore execution.
  https://software.intel.com/en-us/c-compilers/ipsxe
Running on multicore (4 CPU cores)
  GOMC_CPU_GEMC +p4 input file > log file
Biggest performance gains are for GEMC and NPT ensembles, for systems that use the Ewald summation.
  GCMC sees little performance gain on multicore.

## Slide 55: GOMC on GPU
GOMC will automatically detect and compile support for GPUs on Linux if the CUDA development kit is installed.
  https://developer.nvidia.com/cuda-toolkit
GPU executables are named GOMC_GPU_ensemble
GPU executables also include multicore support.
Biggest performance gain is for GEMC for systems that use the Ewald summation.

## Slide 56: GOMC performance
GCMC
GEMC

## Slide 57
Timing data for NVT Monte Carlo simulations of 2,5-dimethylhexane. Data were generated on one core of an i5-3570K 3.40GH Intel(R) CPU or a NVIDIA K40.
Cell List
Move type | Percentage
Displacement | 80
Rotation | 20
Notes: have feature but fastest among other MC codes
in order to achieve this goal, implement cellist
before: loop through all molecule inside sim box, calc distance, rcut => VDW
cellist: looping through surronding box
CPU: 1.7 to 20 times faster 4096 N
GPU: 6 times faster 4096 N

## Slide 58: Parallel Optimization
1
7
4
2
5
8
3
6
9
CPUs
Monte Carlo
Molecular dynamics
Volume move on GPU: O(N2)=> O(N)
All other moves: Not enough work; GPU starves.
Need to create more parallel work.
Notes: MC move one molecule at a time; MD move all molecules at a time.

## Slide 59: Ewald Summation

## Slide 60: GPU Scaling
Volume Move:
+
For
Displace, swap, rotate:
For
Notes: N is number of particles. N2 comes from reciprocal part

## Slide 61: NVT on GPU: Dimethylether
OpenMP: 4 cores
1 CPU core + NVIDA K40 GPU
Notes: Displace and rotation move. 4 CPU openMP vs. 1 CPU and GPU.

## Slide 62: GEMC on GPU: Dimethylether
OpenMP: 4 cores
1 CPU core + NVIDA K40 GPU
Move distribution: 89% displacement, 10% molecule swap, 1% volume transfer
Notes: 50 times faster 4 CPU cores

## Slide 63: Acknowledgements
Mohammad Soroush Barhaghi, Jason Mick, Younes Nejahi, Kamel Rushaidat, Runxuan Jiang, Brock Jackman, Navendu Bhatnagar, Ganesh Kamath, Loren Schwiebert
National Science Foundation CBET-1066661, ACI-1148168, ACI-1642406
NVIDIA, Silicon Mechanics
Grid Computing at WSU

## Slide 65: Argon-Krypton Binary Mixture VLE

## Slide 66: GEMC Ar-Kr Mixture
# Run the GOMC simulation in NVT for 3 million steps.
# Assuming that GOMC base directory was cloned in your Desktop:
~/Desktop/GOMC/bin/GOMC_CPU_GEMC mixture_GEMC.conf > output_Ar_KR.log &
# You can monitor the simulation by running the following command:
tail -f output_Ar_KR.log
# Wait until simulation finished, then exit command by typing "ctrl C"

## Slide 67: GEMC Ar-Kr Mixture
# To extract statistical properties, we can use 'awk' command.
# This command extract and save the mole fraction value for liquid and vapor phase.
cat Blk_AR_KR_GEMC_T_143.15K_BOX_0.dat | awk '{print $1 " " $16}' > molfrac_Ar_liq.dat
cat Blk_AR_KR_GEMC_T_143.15K_BOX_1.dat | awk '{print $1 " " $16}' > molfrac_Ar_vap.dat
cat Blk_AR_KR_GEMC_T_143.15K_BOX_0.dat | awk '{print $1 " " $17}' > molfrac_Kr_liq.dat
cat Blk_AR_KR_GEMC_T_143.15K_BOX_1.dat | awk '{print $1 " " $17}' > molfrac_Kr_vap.dat

## Slide 68: Argon-Krypton VLE at 143.15 K
P (bar) | x1 | y1
4.553 | 0.000 | 0.000
5.619 | 0.040 | 0.212
7.922 | 0.117 | 0.450
10.520 | 0.213 | 0.616
12.941 | 0.295 | 0.700
15.480 | 0.390 | 0.769
18.196 | 0.482 | 0.820
23.451 | 0.665 | 0.893
25.932 | 0.732 | 0.915
28.353 | 0.804 | 0.937
30.834 | 0.878 | 0.960
32.606 | 0.922 | 0.973
36.038 | 1.000 | 1.000

## Slide 69: Simulating different compositions
Need to change the total composition of the system.
Rebuild boxes by changing the number of moles in pack_box_0 and pack_box_1